## Slide 1: VLSM (Variable Length Subnet Mask)
ITE PC v4.0
Chapter 1

## Slide 2: Subnet Questions
The Certkiller Texas branch network is displayed in the following diagram:
Of the following choices, which IP address should be assigned to the PC host?
A . 192.168.5.5
B. 192.168.5.32
C. 192.168.5.40
D. 192.168.5.63
E. 192.168.5.75
ITE PC v4.0
Chapter 1

## Slide 3: Subnet Questions
The Certkiller Texas branch network is displayed in the following diagram:
Of the following choices, which IP address should be assigned to the PC host?
A . 192.168.5.5
B. 192.168.5.32
C. 192.168.5.40
D. 192.168.5.63
E. 192.168.5.75
Answer : C
ITE PC v4.0
Chapter 1

## Slide 4
If a host on a network has the address 172.16.45.14/30, what is the address of the subnetwork to which this host belongs?
A. 172.16.45.0
B. 172.16.45.4
C. 172.16.45.8
D. 172.16.45.12
E. 172.16.45.18
ITE PC v4.0
Chapter 1

## Slide 5
If a host on a network has the address 172.16.45.14/30, what is the address of the subnetwork to which this host belongs?
A. 172.16.45.0
B. 172.16.45.4
C. 172.16.45.8
D. 172.16.45.12
E. 172.16.45.18
Answer : D
ITE PC v4.0
Chapter 1

## Slide 6
What is the IP address range for the first octet in a class B address, in binary form?
A. 10000000-11101111
B. 11000000-11101111
C. 10000000-10111111
D. 10000000-11111111
E. 11000000-10111111
ITE PC v4.0
Chapter 1

## Slide 7
What is the IP address range for the first octet in a class B address, in binary form?
A. 10000000-11101111
B. 11000000-11101111
C. 10000000-10111111
D. 10000000-11111111
E. 11000000-10111111
ITE PC v4.0
Chapter 1
Answer : C

## Slide 8
Which two of the addresses below are available for host addresses on the subnet 192.168.15.19/28?
(Select two answer choices) A. 192.168.15.17
B. 192.168.15.14
C. 192.168.15.29
D. 192.168.15.16
E. 192.168.15.31
F. None of the above
ITE PC v4.0
Chapter 1

## Slide 9
Which two of the addresses below are available for host addresses on the subnet 192.168.15.19/28?
(Select two answer choices) A. 192.168.15.17
B. 192.168.15.14
C. 192.168.15.29
D. 192.168.15.16
E. 192.168.15.31
F. None of the above
Answer : A,C
ITE PC v4.0
Chapter 1

## Slide 10
You have a Class C network, and you need ten subnets.
You wish to have as many addresses available for hosts as possible. Which one of the following subnet masks should you use?
A. 255.255.255.192
B. 255.255.255.224
C. 255.255.255.240
D. 255.255.255.248
E. None of the above
ITE PC v4.0
Chapter 1

## Slide 11
You have a Class C network, and you need ten subnets.
You wish to have as many addresses available for hosts as possible. Which one of the following subnet masks should you use?
A. 255.255.255.192
B. 255.255.255.224
C. 255.255.255.240
D. 255.255.255.248
E. None of the above
Answer : C
ITE PC v4.0
Chapter 1

## Slide 12: How many subnetworks and hosts are available per subnet if you apply a /28 mask to the 210.10.2.0 class C network?
30 networks and 6 hosts.
6 networks and 30 hosts.
8 networks and 32 hosts.
32 networks and 18 hosts.
16 networks and 14 hosts.
None of the above
ITE PC v4.0
Chapter 1

## Slide 13: How many subnetworks and hosts are available per subnet if you apply a /28 mask to the 210.10.2.0 class C network?
30 networks and 6 hosts.
6 networks and 30 hosts.
8 networks and 32 hosts.
32 networks and 18 hosts.
16 networks and 14 hosts.
None of the above
Answer : E
ITE PC v4.0
Chapter 1

## Slide 14: The Certkiller network was assigned the Class C network 199.166.131.0 from the ISP. If the administrator at Certkiller were to subnet this class C network using the 255.255.255.224 subnet mask, how may hosts will they be able to support on each subnet?
14
16
30
32
62
64
ITE PC v4.0
Chapter 1

## Slide 15: The Certkiller network was assigned the Class C network 199.166.131.0 from the ISP. If the administrator at Certkiller were to subnet this class C network using the 255.255.255.224 subnet mask, how may hosts will they be able to support on each subnet?
14
16
30
32
62
64
Answer : C
ITE PC v4.0
Chapter 1

## Slide 16
What is the subnet for the host IP address 172.16.210.0/22? A. 172.16.42.0
B. 172.16.107.0
C. 172.16.208.0
D. 172.16.252.0
E. 172.16.254.0
F. None of the above
ITE PC v4.0
Chapter 1

## Slide 17
What is the subnet for the host IP address 172.16.210.0/22? A. 172.16.42.0
B. 172.16.107.0
C. 172.16.208.0
D. 172.16.252.0
E. 172.16.254.0
F. None of the above
Answer : C
ITE PC v4.0
Chapter 1

## Slide 18
What is the subnet for the host IP address 201.100.5.68/28? A. 201.100.5.0
B. 201.100.5.32
C. 201.100.5.64
D. 201.100.5.65
E. 201.100.5.31
F. 201.100.5.1
ITE PC v4.0
Chapter 1

## Slide 19
What is the subnet for the host IP address 201.100.5.68/28? A. 201.100.5.0
B. 201.100.5.32
C. 201.100.5.64
D. 201.100.5.65
E. 201.100.5.31
F. 201.100.5.1
Answer : C
ITE PC v4.0
Chapter 1

## Slide 20
Which one of the binary bit patterns below denotes a Class B address?
0xxxxxxx
10xxxxxx
110xxxxx
1110xxxx
11110xxx
ITE PC v4.0
Chapter 1

## Slide 21
Which one of the binary bit patterns below denotes a Class B address?
0xxxxxxx
10xxxxxx
110xxxxx
1110xxxx
11110xxx
Answer : B
ITE PC v4.0
Chapter 1

## Slide 22
Your network uses the172.12.0.0 class B address. You need to support 459 hosts per subnet, while accommodating the maximum number of subnets. Which mask would you use?
A. 255.255.0.0.
B. 255.255.128.0.
C. 255.255.224.0.
D. 255.255.254.0.
ITE PC v4.0
Chapter 1

## Slide 23
Your network uses the172.12.0.0 class B address. You need to support 459 hosts per subnet, while accommodating the maximum number of subnets. Which mask would you use?
A. 255.255.0.0.
B. 255.255.128.0.
C. 255.255.224.0.
D. 255.255.254.0.
Answer :D
ITE PC v4.0
Chapter 1

## Slide 24: Using a subnet mask of 255.255.255.224, which of the IP addresses below can you assign to the hosts on this subnet? (Select all that apply)
A. 16.23.118.63
B. 87.45.16.159
C. 92.11.178.93
D. 134.178.18.56
E. 192.168.16.87
F. 217.168.166.192
subnet (0, 32, 64, 96, 128, 160, 192, 224)
and the broadcast address (31, 63, 95, 127, 159, 191, 223).
ITE PC v4.0
Chapter 1

## Slide 25: Using a subnet mask of 255.255.255.224, which of the IP addresses below can you assign to the hosts on this subnet? (Select all that apply)
A. 16.23.118.63
B. 87.45.16.159
C. 92.11.178.93
D. 134.178.18.56
E. 192.168.16.87
F. 217.168.166.192
Answer : C,D,E
subnet (0, 32, 64, 96, 128, 160, 192, 224)
and the broadcast address (31, 63, 95, 127, 159, 191, 223).
ITE PC v4.0
Chapter 1